## Slide 1: B

## Slide 2: Why Connect?

## Slide 3: Remote (and, of course, wireless)

## Slide 4: Flexible

## Slide 5: Today’s Plan

## Slide 6: What do we need to do?
Connect a potentiometer as an input device
Connect an LED as an output device
Copy in some imp firmware

## Slide 7: How does the imp work?

## Slide 8: How does the imp work?
Device 0C2859A
imp service
A
I’m in device 0C2859A!
Here’s the firmware for that device!

## Slide 9: Today’s Schematic

## Slide 10: Breadboard Diagram

## Slide 11: Step 1: Potentiometer
imp pin 8
3.3V
Voltage at imp pin 8 varies between 0V and 3.3V depending on potentiometer position
We read the voltage on pin 8 with an analog-to-digital converter (ADC)
  It’s a 16-bit ADC, so values range from [0,65535]
  We do a little math and send out a number from 0 to 1

## Slide 12: What’s this do?
Potentiometer = a resistive divider with a variable ratio

## Slide 13: What’s this do?
I
In series,

## Slide 14: Step 2: LED
3.3V
GND
An LED is just like a normal diode
  It only conducts current in one direction, and only above a certain internal voltage
  It happens to give off light in the process!
Amount of light varies with current through the diode
Too much current -> POP!

## Slide 15: What’s this do?
3.3V
GND
We use an open drain output on the imp to sink current from the LED
The imp can source or sink up to 4 mA per pin in digital output mode

## Slide 16: What’s this do?
3.3V
GND
  Our diode has forward voltage of about 1.8 V
  Recall we want

## Slide 17: How do we control brightness?
We actually send a pulse width modulated signal to the LED output pin, turning the LED on and off many times a second for varying lengths of time
Your persistence of vision actually does some averaging!

## Slide 18: Step 3: code
Head to plan.electricimp.com, register if you haven’t, and log in
Download the electric imp app from your app store of choice and log in

## Slide 19: Get the code
Open the code tab in the planner and click the “+” button to add a new imp firmware
Name your new firmware and click ok. You’ll go to the imp IDE.

## Slide 20: Add the code
Open a new browser tab and go to https://github.com/tombrew/ei-fw-tom/blob/master/april-brightnessControl.nut
Copy the new code into the IDE and click the save button, then go back to the plan view

## Slide 21: BlinkUp
This is how your imp knows what network to join, how to join it, and whose plan to appear in
Your phone sends the SSID and WiFi password to the imp with a series of “blinks”

## Slide 22: BlinkUp
Log into the electric imp app on your smartphone
Add the local network SSID and password to the app
Hold your phone up to the imp and press “send blinkup”
  If you’re blinking up in a bright place, covering the imp with your thumb reduces ambient light and will help the imp detect pulses

## Slide 23: An imp appears!
The blinked-up imp will appear in your plan
If you haven’t blinked up an imp in this board before, it will say “BLANK”

## Slide 24: Change firmware
Click the settings button in the top right corner of your new impee and select your new firmware from the dropdown menu

## Slide 25: Test
After a second or two, the imp should be running the new firmware
You should see a number inside the impee node in the planner showing the position of your potentiometer

## Slide 26: Test
You can connect your own potentiometer to your own LED to test the LED
  Click the “+” next to the settings button and drag the arrow back to your new impee
  Select the input port in the popup and click “connect”

## Slide 27: Connect imps
Blink up a partner’s imp – now both are in one plan
Draw a connection from one to the other – now one controls the other’s LED!
  Draw another connection in the other direction – now they control each other!

## Slide 28: Imp FW: hardware config
hardware.configure tells a pin what it is
We can declare local variables at global scope to make global variables
server.log sends messages to your log – below the code in the IDE

## Slide 29: Imp FW: Output Ports, functions
Call OutputPort() to create a new output port object with a name – now you can pick this output port in the planner with the “+” button
  Use yourOutputPort.set() to update the value in your new output port
You can declare and call functions, just as you’d expect

## Slide 30: Imp FW: Input Ports, Classes
Extend the InputPort class to conveniently create a new input port – this can now accept new connections in the planner
Implement a set method in your new input class to tell your imp what to do when this input value is changed
The name and type members are shown in the planner when you select the input port to connect to

## Slide 31: Imp FW: wakeup
One of the most useful imp firmware design techniques – to do an action every n seconds, have the function that does that action schedule itself to run again every time it runs
Use imp.wakeup() to schedule this wakeup and callback
Check out http://devwiki.electricimp.com/doku.php for the imp API reference

## Slide 32: Imp FW: configure
imp.configure() registers this impee with the imp service
This function takes three parameters:
  A string to display in the planner to show what the node is (“April Brightness Controller”)
  An array of input ports
  An array of output ports